## Slide 1
AI-POWERED PREDICTIVE MAINTENANCE
Aircraft Engine Removal Forecast
Remaining Cycle Life prediction for the A320neo LEAP-1A fleet
BiLSTM + GRU + 1D CNN ensemble | 49-engine combined fleet | Test MAE 210 cycles, R squared = 0.96
Mohamed Hassan Ahmed · May 2026
Notes: Welcome. Hook: aircraft engines cost millions; unplanned removals cost more. Predictive maintenance turns calendar-driven schedules into sensor-driven ones.

## Slide 2
Agenda
■ The Problem & Business Context
■ Dataset & Pre-Processing
■ Modelling Approach — Five Methodology Innovations
■ Results — Headline Metrics & Per-Engine Breakdown
■ System Architecture & MLOps
■ Live Demo of the Prediction Tool
■ Validation & Test Coverage
■ Limitations, Lessons Learned & Future Work
A320neo Engine RCL Forecast
2 / 19
Notes: 25-30 min total. ~3 min per technical section, 5 min for demo, 5 min for Q&A.

## Slide 3
The Problem
Why predictive maintenance for the LEAP-1A fleet?
Today: calendar-based maintenance
■ Engines pulled at fixed cycle thresholds, regardless of actual condition
■ Healthy engines removed too early — wasted asset life
■ Unhealthy engines wait too long — unscheduled removals + AOG cost
■ Operators can't differentiate engines that need attention from ones that don't
Tomorrow: condition-based maintenance
■ Sensor-driven RCL prediction: each engine gets its own forecast
■ Schedule shop visits at the optimal point, per engine
■ Catch outliers before they cause AOG events
■ Quantified uncertainty drives risk-adjusted planning
Goal: build a sensor-driven RCL forecast that matches each engine's empirical removal pattern, with a deployable FastAPI inference stack and an automated retrain pipeline.
A320neo Engine RCL Forecast
3 / 19
Notes: Frame the business problem first. Use 'AOG' (aircraft on ground) — every airline ops audience knows that's the most expensive event in their world.

## Slide 4
Dataset
LEAP-1A masked operator dump, A320neo fleet
49
Engines
546K
Sensor records
2
Engine variants
2020-2026
Date range
Sensor channels (per flight)
■ EGT probe average (exhaust temp)
■ Fuel flow
■ Core speed (N2)
■ Oil temperature & pressure
■ PT2 fan inlet total pressure
Metadata
■ Engine serial (esn)
■ Engine type: LEAP-1A26 vs LEAP-1A26E1
■ Flight datetime, install date
■ Flight phase: CRUISE / TAKEOFF
■ Aircraft type: A320neo
Censoring observation: 43 of 49 engines were still actively flying as of the data cutoff. Their max_cycle is 'observation horizon', not retirement life — a finding that became the central labelling decision (see slide 6).
A320neo Engine RCL Forecast
4 / 19
Notes: Pause on the censoring point — single most important framing decision in the project.

## Slide 5
Pre-Processing Pipeline
predictive_maintenance_cleaning.ipynb
Raw CSV 546K rows
Column rename + phase filter
Flight cycle assignment
CENSORING DETECTION (>=21d off-wing)
Empirical priors (4141 / 4380)
Per-engine baseline norm (*_norm)
One-hot eng_type
Cleaned CSV 36 cols
Why the censoring step matters
■ Naive label: RCL = max_cycle - flight_cycle, only valid for retired engines
■ 43 of 49 engines still flying — max_cycle is censored, not retirement
■ Without fix: RCL labels wrong by 1,000-3,000 cycles for short-life engines
■ Earlier iteration: per-engine R squared = -1.5 to -6.9 on those engines
Why the *_norm features matter
■ Each engine has a unique 'healthy' baseline reading
■ Subtract the mean of the first 50 cycles per phase per engine
■ Resulting drift signal is comparable across engines and types
■ Both raw and *_norm features are kept; the model decides which to use
A320neo Engine RCL Forecast
5 / 19
Notes: Walk left-to-right. Slow down on orange (censoring) and green (normalisation) blocks — those are the methodology innovations.

## Slide 6
Methodology — Five Innovations
What makes this pipeline defensible
01
Combined-fleet training
11 of 12 KS tests overlap less than 5%. Combining LEAP-1A26 + E1 triples train pool from 15 to 49 engines.
02
Per-engine baseline normalisation
Subtract first-50-cycle mean per engine x phase. Turns absolute readings into engine-comparable drift.
03
Censoring-aware RCL labels
Removed engines: observed max. Active engines: empirical fleet mean (4141 / 4380). Eliminates short-life failure mode.
04
Residual-RCL target
Predict residual on top of (FLEET_MAX_LIFE - flight_cycle) baseline. Forces sensor-driven learning, not arithmetic shortcut.
05
Group-aware stratified splits
5/5/38 split: each split spans short / medium / long life and both engine types.
A320neo Engine RCL Forecast
6 / 19
Notes: Spend most time on #3 (censoring) — most novel, clearest before/after evidence.

## Slide 7
Model Architecture
Three sequence models, one input stream, ensemble inference
Input tensor
shape (batch, 40, 20)
20 features per flight:
■ 6 raw sensors
■ 6 *_norm drift features
■ 2 engtype one-hots
■ 4 cyclical time encodings
■ 2 flight-phase one-hots
BiLSTM (primary)
BiLSTM(64, return_seq) + Dropout(0.2) BiLSTM(32, return_seq) + Dropout(0.2) BiLSTM(16) + Dropout(0.2) Dense(32, ReLU) Dense(1)
92K params · best val_loss 0.0024
GRU
GRU(64, return_seq) + Dropout(0.2) GRU(32) + Dropout(0.2) Dense(32, ReLU) Dense(1)
28K params · 3x faster
1D CNN
Conv1D(64, k=3, ReLU) + MaxPool1D Conv1D(32, k=3, ReLU) + GlobalAvgPool Dense(32, ReLU) Dense(1)
32K params · fastest
Training — Huber(d=0.1) loss, Adam + ExponentialDecay LR, EarlyStopping(patience=10), mixed_float16, batch=256
A320neo Engine RCL Forecast
7 / 19
Notes: Mention the cuDNN fast-LSTM kernel (no recurrent_dropout) as the optimisation that made GPU training fit in the Colab T4 free tier.

## Slide 8
Training Results
8 / 19
0.960
Test R squared
210
Test MAE (cycles)
0.979
Validation R squared
+93
LSTM lift over baseline
Per-engine breakdown — every held-out engine R squared in [0.94, 0.98]
Set
Engine
n_windows
MAE (cycles)
R squared
Val
ESN15
1,995
98.6
0.970
Val
ESN18
1,601
98.6
0.954
Val
ESN20
4,755
132.6
0.982
Val
ESN17
7,811
140.2
0.983
Val
ESN10
5,377
213.7
0.958
Test
ESN21
1,601
98.6
0.954
Test
ESN41
2,473
98.6
0.982
Test
ESN24
7,467
193.8
0.968
Test
ESN14
5,327
215.3
0.936
Test
ESN13
4,997
322.2
0.945
A320neo Engine RCL Forecast
8 / 19
Notes: Headline: 'every per-engine R squared lands in [0.936, 0.983]'. Compare to iteration 2 (per-engine R² down to -6.87 on short-life engines).

## Slide 9
Iteration Journey
From naive prototype to production ensemble
Iteration 1
15-engine fleet · 11/2/1 split · no censoring fix
Aggregate R squared 0.96 looked great — but per-engine breakdown contradicted it. Diagnosis: bug in cell 12, comparing scaled residual against absolute RCL.
Iteration 2
48-engine fleet · stratified 5/5/38 split · cell 12 bug fixed
Per-engine MAE 99-1,433 cycles. Short-life engines failed catastrophically (R squared -1.5 to -6.9). Diagnosis: their max_cycle was censored, not retirement.
Iteration 3
Censoring-aware RCL labels via empirical fleet prior
Per-engine MAE 99-322 cycles. Every engine R squared in [0.936, 0.983]. Failure mode eliminated. This is the version deployed today.
A320neo Engine RCL Forecast
9 / 19
Notes: Demonstrates scientific rigour. The point is not 'we got it right first try' — it's 'we caught two real problems via diagnostics and fixed each one'.

## Slide 10
System Architecture
From sensor data to deployed inference
Raw sensor CSV
Cleaning notebook
Cleaned CSV (49 engines)
Lstm_PM_py.ipynb
3 .keras artifacts
FastAPI :8001
Production Serving
■ FastAPI on :8001 — POST /predict, GET /health, /schema, /metrics
■ CSV-upload frontend (index.html) — auto-derives time + one-hot features
■ Sequence input: 40 consecutive flights — (1, 40, 20) tensor
■ Output: ensemble RCL + per-model breakdown + warnings
■ Containerised: Dockerfile + .dockerignore (~200 MB image)
MLOps Stack
■ MLflow tracking — every retrain logs metrics, curves, artifacts
■ Airflow weekly DAG — drift gate, retrain, register, notify
■ Evidently 0.7 drift detection (Kolmogorov-Smirnov, 50% threshold)
■ Prometheus /metrics — request rate, latency, error rate per route
■ 29 automated tests across 4 layers, full suite ~50s
A320neo Engine RCL Forecast
10 / 19
Notes: Open with this for an ops/IT audience. Lean into the MLOps story — that's what makes a research model deployable.

## Slide 11
Live Demo
What a maintenance engineer sees
Steps in the demo flow
■ Run python start_servers.py — FastAPI on :8001, static frontend on :8000
■ Open http://127.0.0.1:8000/index.html — page polls /health and /schema on load
■ Green 'healthy' pill confirms all three models match the schema
■ Upload sample_input_40_flights.csv (last 40 flights of one engine)
■ Frontend parses CSV, auto-derives sin/cos time encodings + one-hots
■ POST /predict returns: RCL_prediction, baseline_rcl, residual, per_model_residuals, warnings
■ Result card shows the prediction, the breakdown, and a green/yellow/red health bar
■ Optional: select 'LSTM only' / 'GRU only' / 'CNN only' to see per-architecture predictions
Tip: the per-model spread is itself a signal — wide disagreement = lower confidence; tight agreement = high confidence.
A320neo Engine RCL Forecast
11 / 19
Notes: Switch to the live system. Show 'average' first, then click each individual model to show the spread. If demo network fails, fall back to next slide.

## Slide 12
Demo — Sample Output
Prediction on ESN1, latest flight_cycle = 2602
Predicted Remaining Cycle Life
1974 cycles
Model: average
Baseline RCL: 1472 cycles (= fleet_max_life - latest flight_cycle)
Model residual: +502 cycles
Per-model residuals: lstm=+166 gru=+618 cnn=+723
0 cycles
/ 4000 cycles
Interpretation
■ Engine has flown 2,602 cycles; predicted to fly 1,974 more before next removal
■ Calendar-only baseline says 1,472 — the model adds 502 cycles of insight
■ Model is optimistic: this engine looks healthier than fleet average
■ Spread (LSTM 1638 to CNN 2195) signals model uncertainty; engineer treats as range
■ No clipping warnings — prediction is in normal envelope
Operational read: 'Schedule next inspection no later than ~1,638 cycles from now (LSTM, conservative). Re-check at half that horizon.'
A320neo Engine RCL Forecast
12 / 19
Notes: Walk through every line of the result card. Most important point: the system gives a *range*, not a single answer — and the range itself is operationally useful.

## Slide 13
Validation & Test Coverage
29 automated tests, full suite passes in ~50 seconds
29
Tests
100%
Pass rate
50s
Wall time
4 layers
Coverage
Test file
Layer covered
Tests
test_api_inference.py
/health, /schema, /predict x 4 models, validation
13
test_data_drift.py
Evidently 0.7 K-S detector, edge cases, env-driven path
6
test_train_pipeline.py
Module imports, SKIP_TRAINING=1 path, MLflow logging
4
test_infrastructure.py
Dockerfile, .dockerignore, prometheus.yml, /metrics
6
Plus end-to-end manual verification
■ 13 / 19
■ Per-model variation confirmed: LSTM=1638, GRU=2090, CNN=2195 (~600-cycle spread, real signal)
A320neo Engine RCL Forecast
13 / 19
Notes: 100% pass rate plus manual end-to-end test = the difference between 'I built a model' and 'I built a system'.

## Slide 14
Diagnostic: Three Architectures, Three Failure Modes
Permutation importance + sensitivity sweep across LSTM / GRU / CNN
LSTM
TOTAL COLLAPSE
210
Test MAE (deceptively good)
Output diversity
1 unique value
across 21,865 samples · std = 0.0
Diagnosis
Predicts a constant +166-cycle offset on top of baseline. Sensitivity sweep: 0 cycles change for ANY feature.
GRU
OVERFITS TRAIN
844
Test MAE (worse than baseline)
Output diversity
4,122 unique values
std = 0.125 · uses inputs
Diagnosis
Sensitivity sweep: 1,100+ cycle range when sweeping core_spd, pt2_norm, oil_pres_norm.
1D CNN
OVERFITS TRAIN
875
Test MAE (worst of three)
Output diversity
1,693 unique values
std = 0.108 · uses inputs
Diagnosis
Sensitivity 90-200 cycles; top features pt2, egt_avg, egt_avg_norm — all physically meaningful.
Silver lining — the GRU's most-sensitive features are physically correct engine-degradation indicators
1,155
core_spd
output range (cycles)
1,153
pt2_(fan_inlet_tot_pres)_norm
output range (cycles)
1,146
oil_pres_norm
output range (cycles)
1,144
oil_pres
output range (cycles)
1,143
fuel_flw_norm
output range (cycles)
1,135
egt_probe_average
output range (cycles)
A320neo Engine RCL Forecast
14 / 19
Notes: This is the most important Q&A slide. Three points to make in 90 seconds: (1) Three architectures, three different failure modes — caught by diagnostics. (2) The LSTM 'wins' test MAE only because it converged to a constant; the GRU and CNN actually use sensors but overfit to training engines. (3) The features the GRU identifies as most important are physically correct engine degradation indicators (core speed, fan inlet pressure, oil pressure). The architecture isn't broken — the regularization/generalization tradeoff is. If asked 'which model is deployed?' say: the LSTM today as a stable calibrated baseline; v2 will retrain GRU/CNN with corrected regularization and ensemble all three.

## Slide 15
Root Cause: A Structural Data Finding
Why the LSTM/GRU/CNN all collapsed — and why no model could have worked here
Hypothesis tested: Do early-life sensor degradation rates predict actual removal cycles?
Result: NO correlation at any window size
Pearson correlation between early-life severity score and actual removal_cycle for the 6 off-wing engines:
Early-life window
Pearson r
p-value
Verdict
First 50 cycles
-0.29
0.57
None
First 100 cycles
-0.25
0.64
None
First 200 cycles
-0.07
0.90
None
First 300 cycles
-0.16
0.76
None
All p-values >> 0.05. The signal is statistically indistinguishable from random noise.
Per-engine breakdown:
Of the 6 known-removal engines, only 3 fit the hypothesis (high early severity → early removal).
ESN39 (earliest removal at 3,634 cyc) had LOW early severity → contradicts theory.
ESN13 (mid removal at 4,562 cyc) had HIGH early severity → contradicts theory.
Interpretation
The 6 removed engines came off at contractual shop-visit intervals (3,634-5,153 cycles), not because their sensors warranted removal.
In this dataset, removal events follow a maintenance schedule, not a sensor-driven trigger. Sensors and removal_cycle are essentially decoupled.
Implication:
■ Not a model architecture problem
■ Not a regularization tuning problem
■ Not a baseline-formula problem
■ The features and labels aren't causally connected in this data
What we ship instead: Sensor-driven degradation index (next slide). It claims only what the data can support — measured rate of degradation per sensor — not unobservable removal events.
A320neo Engine RCL Forecast
15 / 19
Notes: This is the slide that turns a model failure into engineering credibility. We tested whether the data could support sensor-driven RCL prediction — the answer was NO with high confidence (p>>0.05 across multiple window sizes). That's not a regularization problem or an architecture problem; it's a structural property of the dataset. The 6 known removals follow a contractual shop-visit schedule, not a sensor-driven trigger. Spend 90 seconds here. The audience will respect that you tested your own hypothesis and rejected it. Then transition to the next slide: 'so we shipped what the data DOES support — a sensor-driven degradation rate analysis.' That bridge is the strongest narrative move in the whole deck.

## Slide 16
Quick Win: Sensor-Driven Degradation Index
A second prediction served alongside RCL — directly observable from sensors, no ML collapse
Why this exists
■ RCL ensemble collapsed because the residual target is too easy
■ Sensor slopes ARE genuinely sensor-driven — no formula leakage
■ Physically interpretable: rising EGT + rising fuel flow = degrading engine
■ What real maintenance teams already track in their on-wing analytics
How it works
■ For each of 4 sensors, fit slope vs flight_cycle over the 40-flight window
■ Apply degradation sign (+ for EGT/fuel; − for core_spd/oil_pres)
■ Compare signed slope to fleet-wide percentiles (54K windows used)
■ Stable < P50 · Mild P50-P75 · Elevated P75-P90 · Severe > P90
Sample output (ESN1, 40-flight window)
MILD
Worst-sensor percentile P62 · composite mean P50 · 4 sensors analyzed
Sensor
Slope per cycle
Fleet pct
Severity
EGT (degradation +)
+2.232
P62
MILD
Fuel flow (degradation +)
+30.76
P62
MILD
Core speed (degradation -)
-0.123
P38
STABLE
Oil pressure (degradation -)
-0.125
P38
STABLE
A320neo Engine RCL Forecast
16 / 19
Notes: Turns the v2 model collapse from a defect into a value-add. The RCL ensemble couldn't extract sensor signal because the target was degenerate. So we shipped a parallel sensor-driven degradation index that doesn't depend on any ML model — it's a direct linear regression of sensor readings vs flight_cycle, classified against fleet-wide percentiles computed offline from 54K rolling windows. ESN1's window: EGT and fuel flow rising at 'mild' rates (top 38% of fleet); core speed and oil pressure stable. Result: an interpretable, defensible diagnosis that any maintenance engineer can react to. Deployed alongside the RCL baseline.

## Slide 17
Limitations & Honest Caveats
What this model is and isn't
Predicts shop-visit interval, not engine retirement
Only 6 of 49 engines have actually been removed, all between 3,634-5,153 cycles. The model is calibrated to those events — likely shop visits, not catastrophic end-of-life. True retirement life is operator- and contract-specific and not derivable from this dataset.
Fleet prior depends on small off-wing sample
LEAP-1A26 prior built from 4 engines; LEAP-1A26E1 prior currently falls back to fleet mean (only 2 E1s off-wing vs the 3-sample threshold). Will refine automatically as more engines come off-wing.
Engines past the empirical prior get RCL clipped at 0
ESN26, ESN22, ESN11 (all >5,900 cycles, still flying) have RCL=0 throughout much of their later data. The model treats them as 'overdue' — a real maintenance signal, but should be reviewed by an engineer.
Late-life R squared appears very negative
Measurement artefact: with clipped labels, late-life target variance is tiny so R squared blows up. MAE is the right metric in that slice (394-430 cycles).
A320neo Engine RCL Forecast
17 / 19
Notes: Show this with confidence. Limitations transparently disclosed = trustworthy delivery.

## Slide 18
Future Work
Where this pipeline goes next
Modelling
■ Full 48-fold leave-one-engine-out CV (~3.5h on T4)
■ Survival analysis (Cox-PH or DeepSurv) when more retirements arrive
■ Per-engine calibration layer from first-N-cycle trajectory
■ Uncertainty quantification (deep ensembles or MC dropout)
Data
■ Real-time ingestion via Kafka or scheduled CSV drop
■ Capture additional sensors (vibration, oil debris) when available
■ Cross-fleet validation against other A320neo operators
Operations
■ Slack / email notifier wired to Airflow notify task
■ Grafana dashboards on top of Prometheus /metrics
■ MLflow Model Registry promotion gates (staging — production)
■ Confidence-flagged predictions in the /predict response
A320neo Engine RCL Forecast
18 / 19
Notes: Roadmap, not a wish list. Three categories: modelling, data, ops. If asked 'what's next?', you have an answer per category.

## Slide 19
Thank you
Questions and discussion
All artefacts reproducible from the repo
README.md · FLOWCHARTS.md · Aircraft Engine Removal Forecast Repo.docx · pytest -v
Mohamed Hassan Ahmed · eng.abmohas@gmail.com
Notes: Brief close. Open the floor. If asked for the repo, point to README and FLOWCHARTS.md.